## Slide 1
Attendance Scan In
Valid within 15 mins before scheduled start time of the oral presentation
NTU PhD students (for Seminar Records purposes)
NTU Faculty/Staff (if requires attendance record)
DO NOT circulate the QR/Link code.
MUST attend the whole session.
Else disciplinary action will be taken.
https://forms.office.com/r/U4DV4KrmPs

## Slide 2
Distributed Edge Intelligence Enabling Framework
for IoT-based Structural Health Monitoring
Speaker: Cui Shuaiwen | Supervisor: Asst. Prof. Fu Yuguang
Notes: Good afternoon, everybody! Welcome to my QE oral presentation.
My name is Cui Shuaiwen, and I am supervised by Assistant Professor Fu Yuguang.
As shown here, my PhD researchis about a distributed edge intelligence enabling framework which is specially designed for low-cost and resource-constrained edge devices in IoT-based structural health monitoring.

## Slide 3
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHM
Advantages
Low Cost
Ease of Installation & Maintenance
Support for Customization
Real-time Performance
Edge Computing
Structural Health Monitoring (SHM) & Internet of Things (IoT)
Introduction – Structural Health Monitoring (SHM) & Internet of Things (IoT)
Front End
IoT-based SHM
Back End
sensor
gateway
server
Challenges
Constrained Power
Supply
Limited Onboard Computing Resources
Network Latency
Insufficient Automation
Lack of Tools / Libraries
Numerical Errors
Notes: Let’s start the journey with Structural Health Monitoring and the Internet of Things.
SHM refers to the process of using a series of devices and analytical techniques to monitor, assess, and evaluate the performance of the target structures for decision-making.
Nowadays, SHM is deeply combined with IoT technologies. And a typical IoT-based SHM system features a frontend and a backend, including sensor, gateway, and remote server.
The prevalence of IoT-based SHM systems is based on it attractive advantages, including:
The low cost
edge computing capability
real-time performance
ease of installation and maintenance
support for customization
But at the same time, it is also suffering from many long-standing challenges, including
Limited Onboard Computing Resources
Limited Power Supply
Network Latency
Insufficient Automation
Lack of Tools / Libraries
Numerical Errors
This study targets on the first two challenges:
For the limited onboard computing resources, our solution is to develop lightweight edge computing and edge AI.
For the constrained power supply, there are two ways: one way is to increase power supply, like energy harvesting, but the problem is it may not be stable or enough. So we adopt the other way, which is to reduce power consumption by using power-saving hardware and software designs.

## Slide 4
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Distributed Edge Intelligence & Research Gap
Introduction – Distributed Edge Intelligence & Research Gap
Centralized Computing Distributed Computing
State of the Arts & Research Gaps
2 General-purpose vs Domain-specific Development
General-Purpose
Frameworks
SHM-Specific
Frameworks
Project-Oriented
Product-oriented
3 Project-oriented vs Product-oriented Development
1 Microprocessor (MPU) vs Microcontroller (MCU)
MPU-Level Devices
MCU-Level Devices
Powerful
Expensive and Power-Hungry
Resource-Constrained
Cheap and Power-Saving
Advantages
Workload & Expenses
Transmission Payload
Power Consumption
Response Latency
Notes: Then, let’s talk about computing paradigms.
Conventional IoT-based SHM systems adopt centralized computing, where almost all computational tasks are performed on the central server, featuring high latency and power consumption.
(2) In contrast, decentralized computing paradigm is to properly distribute computational tasks over the whole system so that the computational resources of the whole system can be utilized.
There are many advantages using distributed edge intelligence: the workload & expenses, transmission payload, power consumption, and response latency can be reduced at the same time at the cost of increased workload on the edge devices.
Regarding the state of the arts, I have identified several research gaps:
The first one is the gap between MPU devices to MCU devices. Many studies claimed to achieve edge intelligences but only turned out to be using MPU devices like Raspberry Pi or Nvdia Jetson series. MPU devices are powerful and easy for AI deployment, yet expensive and power-hungry, not suitable for long-term and large-scale SHM applications. In contrast, MCU devices is resource-constrained, yet cheap and power-saving, suitable for SHM.
The second one is the gap between the general-purpose development to domain-specific development. Currently, few frameworks focus on SHM, not to mention the support for edge intelligence enabled SHM.
The third one is the gap between the project-oriented development to product-oriented development. Many studies develop their nodes using a project-oriented manner rather than in a product-oriented manner, the framework in this study is going to be modularized and layered, easy for cross-platform reuse.

## Slide 5
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Research Scope and Outline
Introduction – Research Scope and Outline
Prototype Development
Algorithm Development
Frontend
MCU
Sensing
Network
UI
Hardware
Software
Middleware
App
Backend
Computing
Brokering
Analyses
Storage
Connection
Control
Smart Adaptive Triggering Mechanism
- Threshold
- Duration
Feedback Control
Digital Twin
Edge AI
False Trigger
Missed Trigger
Federated Learning for Event Classification
Classify
Ambient Vibration
Impact
Earthquake
Strong Wind
More …
TinySHM
…
Computing
SHM
Misc.
math
DSP
AI
BMS
FS
commu.
sensing
sys. id.
damage detection
Support
Drive
Notes: Before you lose your patience, lets me outline my research contents.
My efforts for this study can be divided into two parts: Prototyping Development and Algorithm Development. These two parts support and drive each other.
So, a sensing platform development should have a frontend and a backend. And I do want to highlight that, the framework is embodied as a part of the middleware of the front end. For short, it is named as TinySHM. It features the capability of edge computing and intelligence, and specially designed for SHM.
As for algorithm development, there is no way to cover every topic in SHM. So, what I am doing here is to focus on several typical and important issues.
The first topic is to design a smart adaptive triggering mechanism to fine-tune triggering parameters for low false trigger and low missed trigger rates. And this topic is single-node level issue.
The second topic is a multi-node level issue, required coordination. It is about federated learning of event classification in SHM, and it has the potential to reduce transmission overhead and power consumption.
(3) In future, there will more …

## Slide 6
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Innovations and Contributions
Introduction – Innovations and Contributions
Prototype Development
Algorithm Development
Low-power Low-Cost Edge Devices
Long-Term
Large-Scale
Autonomous
Product-Oriented
Layered Architecture & Modularized Design
Edge Computing & Intelligence
Careful HW Selection & SW Integration
Lightweight Design
Smart Adaptive Triggering Mechanism
Adaptive Fast-convergence to Optimal Triggering Configurations
Methods: Feedback Control, Digital Twin, NN, Bayesian Optimization
Federated Learning Workflow for Event Classification
Low Transmission Payload and Low Power Consumption
Domain-Specific, Specially for SHM
for Structural Health Monitoring
Notes: Innovations and Contributions
For the prototype part:
(1) It is designed for low-power low-cost edge devices
(2) It is developed in a product-oriented manner
(3) It is domain specific, specially for SHM
(4) It supports edge computing and intelligence
As for the algorithm part:
For the adaptive triggering mechanism, we have achieved adaptive fast-convergence to optimal triggering configurations.
We have proposed a federated learning workflow for event classification featuring low transmission payload and low power consumption.

## Slide 7
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Introduction – Table of Contents
01
Prototype Development
03
Federated Learning for Event Classification
02
Smart Adaptive Triggering
04
Conclusions & Plans
Notes: The rest of this presentation will be organized in four chapters, with the first one about prototyping, the second and third one about algorithm development, and the last chapter is about conclusions and future plans.

## Slide 8
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development
01
Prototype Development
03
Federated Learning for Event Classification
02
Smart Adaptive Triggering
04
Conclusions & Plans
Notes: Let’s move onto the first chapter, which is about the prototype development.

## Slide 9
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development – Sensing Platform Prototyping
1-1 Sensing Platform Prototyping
Sensing
Storage
Computation
Communication
Internet
Coordination
Computation
Storage
Analysis
Interfacing
LiftNode
LiftHub
Frontend
Backend
Notes: As an IoT sensing platform, the prototype should have a frontend and a backend. Since this research is mainly about distributed edge intelligence, therefore the front end is mainly in charge of sensing and computation while the backend is only mainly in charge of coordination.
Given the importance of the edge computing, I will focus on the frontend today.

## Slide 10
TinySHM
LiftNode
Sensor
Framework
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development – Hardware Development - Architecture
Support
Enable
MAIN CONTROL
PERCEPTION
COMMUNICATION
INTERACTION
POWER
1-2 Hardware Development - Architecture
Notes: Before delving deeper, I want to highlight two major ideas in this chapter, namely, the sensor prototye LiftNode, and the enabling framework, TinySHM. As shown here, LiftNode supports TinySHM. And TinySHM in turn enables the sensor LiftNode.
The sensor can be abstracted as the combination of 5 sub-systems, including the main control, perception, communication, interaction, and power system.

## Slide 11
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Main Control
Micro Controller Unit
Timer/ RTC
RAM/ROM Memory
SPI/I2C/UART/ADC/DAC/…
Large Volume Storage
Perception
Communication
Interaction
Blue Tooth
Zigbee
WIFI
Cellular Network
Command Input
Status Monitoring
Vibration
Strain
Camera
Temperature &Humidity
…
Power System
Battery / Power Outlet
Power Management System
Local Communication
Internet Communication
01 Prototype Development – Hardware Development - Architecture
1-2 Hardware Development - Architecture
Notes: Each of these sub-systems is composed of many different components, and the development is still ongoing.

## Slide 12
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development – Hardware Development – MCU & Main Control Board
1-3 Hardware Development – MCU & Main Control Board
MCU Selection
Espressif - ESP32
ESP32-S3
Toolchain
AI Support
ESP-IDF
ESP-DL
ST Electronics - STM32
STM32H743
Toolchain
AI Support
STM32CUBE
X-CUBE-AI
Main Control Board Selection
Alientek - DNESP32S3M Devkit
MCU
LED
RAM
IO
ROM
Button
TF Card
Screen
ESP32-S3
Dual-Core
240MHz
SRAM: 512 KB
PSRAM: 8 MB
ROM: 384 KB
FLASH: 16 MB
Up to 32 GB
Power: 1
User: 1
PIN: 36
RESET 1
BOOT/USER 1
0.96’’ LCD
Fanke - STM32H743IIT6 Devkit
MCU
LED
RAM
IO
ROM
Button
TF Card
STM32H743
480MHz
SRAM: 1 MB
SDRAM: 32 MB
ROM: 2 MB FLASH: 8 MB
Up to 32 GB
Power: 1
User: 1
PIN: 112
RESET 1
BOOT/USER 1
~ 20 SGD
~ 24 SGD
Notes: To facilitate the prototyping, I investigated several major MCU brands ESP32 and STM32. Both of them are famous for good toolchain and support onboard AI.
And then I selected to main control boards built upon these two microprocessors. And if you check the computational related resources, you will find they are very typical MCU-level devices. Apart from that, they are very cheap, only around 20 SGDs, that can give you some idea why MCU devices are suitable for large scale uses.

## Slide 13
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development – Hardware Development – LiftNode Prototypes
1-4 Hardware Development – LiftNode Prototypes
ESP32
STM32
ATK DNESP32S3M
FANKE STM32H743
Notes: Shown here are the physical prototypes using ESP32 and STM32.

## Slide 14
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development – Software Development – Architecture
1-5 Software Development - Architecture
Main
Control
Peripheral Components
Sensing / Communication / Interaction / Power Supply
Startup Code
Hardware Abstraction Drivers (Register-Level)
Board Support Packages
(Board-Level)
Real-time Operating System (RTOS)
TCP/IP & MQTT
File System
Digital Signal Processing
Edge AI Framework
Edge Intelligence Library for SHM Applications - TinySHM
Math
DSP
Network
AI
Measurement
System Identification
Damage Detection
Config
Sense
File
Notification
…
Application Specific Code
Hardware
Application
Middleware
RTOS – Task Scheduling
FS – File Operation
TCP/IP & MQTT – Internet Communication
DSP/AI – Onboard Computing
TinySHM – Commonly Used Functions in App Layer
Drivers
Platform-specific
Notes: Now it’s to move onto the software architecture. It adopts a typical 4-layer architecture.
The bottom layer is the hardware layer, standing for the physical components.
And second to last layer is the driver layer, which is platform-specific.
On top of that is the middleware layer, including many high-level functions. Most importantly, the framework TinySHM is in this layer.
The top layer is the application layer.

## Slide 15
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development – TinySHM
1-6 TinySHM
TinySHM Math
Matrix Multiplication
Convolution
Eigen Value Computation
Singular Value Decomposition
…
Up-sampling & Down-sampling
Discrete Wavelet Transform
Independent Component Analyses
…
TinySHM AI
Gaussian Process Regression
Stochastic Process Control
Convolutional Neural Network (CNN)
Dense Neural Network Predictor (DNN)
Main
Control
Peripheral Components
Sensing / Communication / Interaction / Power Supply
Startup Code
Hardware Abstraction Drivers (Register-Level)
Board Support Packages
(Board-Level)
Real-time Operating System (RTOS)
TCP/IP & MQTT
File System
Digital Signal Processing
Edge AI Framework
Edge Intelligence Library for SHM Applications - TinySHM
Math
DSP
Network
AI
Measurement
System Identification
Damage Detection
Config
Sense
File
Notification
…
Application Specific Code
TinySHM DSP
Notes: The TinySHM framework features many modules for different tasks. And here, I would like to focus on the modules related to computation and AI for SHM.
Unlike on computer, few people will try edge computing on MCU devices not to mention SHM. So, I need to develop the tools by myself.
Listed here are the functions summarized from some past projects using edge computing. For example:
For math operations, there are matrix multiplication, convolution, eigen value computation, and etc.
For digital signal processing, there are resampling, wavelet transform, independent component analyses, and etc.
For AI, there are Gaussian Process Regression, CNN, DNN

## Slide 16
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
01 Prototype Development – Unit Tests
1-7 Validation in Applications
Data Collection
MATH/DSP
AI
Onboard Wavelet Transform (WT)
Sudden Damage Detection
Data-driven Anomaly Detection
Notes: You may wonder whether the porotype can be used for real applications, and here are some examples.
The left part is about data sensing in chapter 2.
The middle part is about damage detection using wavelet transform.
The right part is about anomaly detection using Gaussian Process Regression, showing a good match with PC results.

## Slide 17
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering
01
Prototype Development
03
Federated Learning for Event Classification
02
Smart Adaptive Triggering
04
Conclusions & Plans
Notes: Chapter 2 is about a smart adaptive triggering mechanism.

## Slide 18
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Sensing Schemes and Event-Trigger Sensing
2-1 Sensing Schemes and Event-trigger Sensing
Always-on
Duty-cycle
Event-triggered
active
inactive
events of interest
partially miss out
inactive miss out
low power miss out
Notes: For SHM, many devices run on batteries, so power efficiency is super important.
If sensors stay on all the time, the battery will drain quickly.
To save power, we can use duty-cycling, where sensors wake up periodically. But the downside is, they might miss important events while sleeping.
That’s why event-triggered sensing was introduced, where sensors only wake up when required, saving power while capturing critical data.

## Slide 19
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Trigger Sensing Mechanism
2-2 Trigger Sensing Mechanism
Sentry Mode: Low Power, Low Resolution
Working Mode: High Power, High Resolution
ADXL362
resolution: 12-bit
power consumption:
1.8uA (sensing, 100Hz) ; 270nA (sleep)
LIS344
resolution: 24-bit
power consumption:
~ 5mW (sensing); 3uA(sleeping)
ADXL362
LIS344
Xnode - Trigger Sensing Mechanism
Low-power Sensor + High-resolution Sensor
Trigger Sensing Mechanism
Activation
Duration
Activation
Threshold
Deactivation
Duration
Deactivation
Threshold
Triggering Parameters:
Threshold: absolute value, continuous
Duration: number of sampling points, discrete integers
A Two-class Classifier
make mistakes, to be improved
Notes: How can we achieve event-triggered sensing? Let me use the XNode as an example.
It involves two sensors: a low-power, low-resolution sensor and a high-power, high-resolution sensor. These sensors operate in two modes, sentry mode and working mode.
In sentry mode, the low-power sensor monitors for events of interest. Once detected, the system switches to working mode, waking up the high-resolution sensor to collect detailed data.
On the right-hand side, you can see how the triggering mechanism works: when the input signal exceeds the threshold for a certain duration, the high-resolution sensor is activated. Essentially, this is a two-class classifier.
As a classifier, it make mistakes, and is remained to be improved.

## Slide 20
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Triggering Mechanism Performance
2-3 Triggering Mechanism Performance
Confusion Matrix
False Positive (FP)
[TYPE I]
False Trigger
True Positive (TP)
Ground Truth
Prediction
True Negative (TN)
False Negative (FN)
[TYPE II]
Missed Trigger
positive
positive
negative
negative
Objective
Minimize Missed Trigger
False Trigger at Low Level
Optimal Configuration for
precision
recall
Multi Objective Problem
Trade-off Required
Notes: To improve this mechanism, we first need to characterize its performance. We can use a confusion matrix.
There are two types of errors we care about: false triggers and missed triggers. To assess these errors, we use two associated metrics: precision and recall.
The goal is to minimize missed triggers while also keeping false triggers low. But there’s a trade-off between these two objectives.

## Slide 21
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Challenges & Potential Enablers
2-4 Challenges & Potential Enablers
Lack of Adaptivity
Preconfigured Parameters
Fixed Values
Feedback Control & Bayesian Optimization
Multiple Objective
Multiple Objectives
Trade-off Required
Comprehensive Metric
Unknown / Imbalanced Data
Unknown & Imbalanced
Data Distribution
Artificial Distribution & Digital Twin
No Ground Truth
No Ground Truth for Captured Events
Edge AI for Classification
Partial Observability
No information of uncaptured events
Edge AI for Prediction
Costly Feedback
Long-term / Costly to Capture Enough Records
Digital Twin
Summary
Closed Loop Control
Backbone for Adaptivity
F-beta
Digital Twin
Data Augmentation
Feedback Acceleration
Pre-Optimization
Neural Networks
Ground Truth Estimation
Unobservable Value Estimation
Bayesian Optimization
Parameter Optimization
Fast Convergence
Notes: We have several critical challenges, but accordingly, we can find some solutions to deal with them.
First, lack of adaptivity: Triggering parameters are fixed and can’t adapt to the environment. To solve this, we can use feedback control or Bayesian approaches to optimize parameters based on observations.
Second, as mentioned, this is a multi-objective problem: A comprehensive metric can help balance these objectives.
Third, the input data to the triggering mechanism is unknown and may be imbalanced. This means our evaluation can be quite difficult. One solution is to use artificial dataset.
Fourth, We have no ground truth for the captured events on the edge. We can use AI for estimation.
Fifth, Observability Issues: Since only triggered events are captured, we don’t know how many are missed. We can also use AI for estimation.
Finally, Costly Feedback: Capturing enough data for evaluation can be time- and power-consuming. We can use digital twin to accelerate.
In summary, we can jointly use closed-loop control, digital twins, neural networks, and Bayesian optimization, to form a comprehensive solution.

## Slide 22
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Smart Adaptive Triggering Mechanism (SATM)
2-5 Smart Adaptive Triggering Mechanism (SATM)
Closed Loop Control
Multi-Stage Deployment
1 Environment
structure response under different events
2 System
triggering mechanism (threshold & duration)
3 Estimator
Metric harmonizing recall & precision
4 Controller
Bayesian Optimization
1 Environment
2 System
4 Controller
3 Estimator
ref
F-beta
response
parameters
TP/FP/FN
Stage I
Initialization
Stage II
Digital Space Optimization
Stage III
Real World Optimization
Stage I
data synthesizing using digital twin
neural network training
Stage III
onboard fine-tuning using edge intelligence
Stage II
preliminary optimization in digital twin
Notes: Given the importance of adaptivity, we can use closed loop control as the backbone.
As shown, the closed-loop control model has four major components: Environment, System, Estimator, and Controller. I will introduce them one by one later.
As for deployment, to accelerate onboard optimization, we can use digital twin, and we can divide the process into digital space optimization and real-world optimization. Digital space is for preliminary optimization and the real world for fine-tuning. Apart from these two stages, we need an initialization stage for preparation.

## Slide 23
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – The Closed Loop Control (Feedback Control)
2-6 The Closed Loop Control (Feedback Control)
1 The Environment
2 The System
Ambient Vibration
Impact
Earthquake
Strong Wind
Excitation
Structure Response
Structure
Physical
Structure
Digital
Twin
Equation of Motion
Newmark Beta
Structure Response
Response
Real
Virtual
The Triggering Mechanism
Triggering Parameters:
Threshold: absolute value, continuous
Duration: number of sampling points, discrete integers
[DIGITAL TWIN]
Notes: The environment component refers to the structure responses. This is also where digital twin comes into play.
As you can see, we started with excitations of different event types, including ambient vibration, earthquake, impact and strong wind. Then the structures, both the physical and the digital twin. Note that the digital twin is modeled by the equation of motion and Newmark beta method. Finally, we have the response from the real and virtual spaces.
The system component, which, in our case, refers to the triggering mechanism itself, which is based on threshold and duration.

## Slide 24
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – The Closed Loop Control (Feedback Control)
2-6 The Closed Loop Control (Feedback Control)
3 The Estimator
4 The Controller
The Performance Metric
balances recall and precision
Esimator in Real World
F-beta
TP, FP
Precision
Recall
CNN Classsifier
DNN Predictor
Esimator in Digital Twin
Precision
Recall
F-beta
TP
FP
FN
The Engine for Optimization
threshold
duration
Black Box Problem
Expensive Evaluation
Bayesian Optimization
Bayesian Optimization Algorithm Framework
Require：
for to T do
InitSample()
p() FitModel()
end for
function / variable domain / acquisition function / surrogate model
initialize the observation set
surrogate model regression
determine next point to investigate
get corresponding value
update the observation set
[NEURAL NETWORKS]
[BAYESIAN OPTIMIZATION]
Notes: [ESTIMATOR]
The estimator is used to provide a performance metric to evaluate the system component. This is also where NN comes into play.
For this, we use the F-beta score, a machine learning tool that balances precision and recall by tuning the beta value.
The estimator operates differently in the digital twin stage and the real-world deployment stage:
In the digital twin stage, everything is known, so the F-beta score is calculated using upstream metrics like TP, FP, and FN.
In the real-world stage, a CNN model is used to provide ground truth label, and a DNN model is used to estimate Recall due to observability issues.
[CONTROLLER]
The controller is the engine for optimization. We use Bayesian Optimization for the controller.
So why we use it?
Blackbox problem
Expensive Evaluation
The key idea of Bayesian Optimization is that it uses a surrogate model to approach the objective function.
And it is an iterative process, for each iteration, it determines the next point to observe by balancing exploration and exploitation.
Another desirable feature is that the whole process can be characterized and recorded by the observation dataset. This is also the key why we can divide the process into multi stages.

## Slide 25
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Multi-Stage Deployment Strategy
2-7 Multi-Stage Deployment Strategy
Structures
real
virtual
Responses
real
virtual
Stage I - Initialization
Data Synthesization
NN Training
Events
CNN classifier
DNN predictor
Features
Labels
Recall
Noise
Threshold
Duration
Stage II – Digital Space Optimization
Digital Space Response
Triggering Mechanism
TP/FP/FN
Bayesian Optimization
(Preliminary)
Precision
Recall
ref
F-beta
response
parameters
Stage III – Real World Optimization
Real World & Digital Space Response
Triggering Mechanism
CNN
Bayesian Optimization
(Fine-tuning)
DNN
Precision
Recall
ref
F-beta
response
parameters
Notes: The deployment is divided into three stages:
STAGE I - INITIALIZATION There are two major tasks:
Data Synthesization: To prepare the dataset used in NN training and subsequent stages.
Neural Network Training: Train a lightweight CNN-based classifier and a DNN-based predictor for stage III.
STAGE II – DIGITAL SPACE OTPIMIZATION This stage is mainly for reducing the workload of real-world optimization. Basically, the optimization is conducted in virtual environment. And the results can be directly applied to stage III for fine-turning.
But this assumes that the data distribution in the virtual world is close to the one in real world. And the key is to ensure the simulated data aligns with real-world characteristics, especially for ambient vibration, like average amplitude and standard deviation.
STAGE III – REAL WORLD OPTIMIZATION
This stage is for trigger parameter fine-tuning.
There are some difference from stage II that you might have noticed.
- The dataset is mixed, from both the real world and the digital space.
- The precision and recall are provided directly or indirectly by edge AI.

## Slide 26
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Validation – Laboratory Test Setup
2-8 Validation – Laboratory Test Setup
Structure Model
LiftNode (STM32-based)
Ambient Vibration
Impact
Strong Wind
Earthquake
Notes: To validate the proposed smart adaptive triggering mechanism, laboratory tests were conducted, as shown here.
Here are the model structure and the sensor prototype for data collection. For different events, there are different ways for simulation.

## Slide 27
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
02 Smart Adaptive Triggering – Validation – Stage I: Initialization
2-8 Validation – Stage I: Initialization
Dataset Synthesizing
Ambient Vibration
Impact
Earthquake
Strong Wind
1000 records 60s@100Hz
1000 records 60s@100Hz
1000 records 60s@100Hz
1000 records 60s@100Hz
Lightweight Neural Network Training
Test Acc 99.55%
CNN
DNN
Notes: [DATA SET]
1000 records (each 60 seconds at 100 Hz) were synthesized for each event type.
[NN]
A classification network to provide ground truth for event detection.
A recall estimation network to predict recall values.
On the right are the architectures and training curves of these neural networks. As shown, both are lightweight and powerful.

## Slide 28
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
02 Smart Adaptive Triggering – Validation – Stage II: Digital Space Optimization
Optimization in Digital Twin
duration
threshold
duration
threshold
Objectives:
Rough Model between Triggering Parameters and Performance
Save Resources for Real-world Optimization
Dataset:
Ambient Vibration: 600 records (same level of real world)
Impact, Earthquake, Strong Wind 200 records each from Stage I Dataset
Procedures:
Initialization: 15 random observation points
Iteration: 30 observation points
2-8 Validation – Stage II: Digital Space Optimization
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
Notes: For stage II, as shown on the right-hand side, in the digital space, 15 points were randomly generated for initialization, and 30 points were generated for iterative optimization.
It can be seen that the points gradually aggregate at a small area with high F-beta score.
Stage II focuses on roughly modeling the data distribution and performing preliminary optimization of the triggering parameters.
In this stage, 600 records of ambient vibration and 200 records each for impact, earthquake, and strong wind were used for optimization.
As shown on the right, the process starts with 15 random observation points for initialization, followed by a 30-point iterative optimization. To speed up the process, a bonus factor was applied in cases where both recall and precision exceeded 0.9. Otherwise, the theoretical maximum score was capped below 1.

## Slide 29
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
02 Smart Adaptive Triggering – Validation – Stage III: Real World Optimization
duration
threshold
duration
threshold
Objectives:
Fine-tuning Triggering Parameters Using Real-world Feedback
Dataset:
Ambient Vibration: 150 records from real world
Impact, Earthquake, Strong Wind 50 records each from Stage I Dataset & Gradually Replaced by Collected Data
Procedures:
Iteration: 20 observation points
2-8 Validation – Stage III: Real World Optimization
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
Optimization in Real World
Notes: For stage III, as shown on the right-hand side, 20 more points were observed for fine-tuning optimization. There are two key points can be observed.
First, the red dots and the blue dots share similar peak values at similar area. This is to say the data distribution is quite close.
Second, the average score for blue dots is significantly higher than the red ones. This is to say that the pre-optimization in stage II is effective.
Stage III focuses on onboard fine-tuning, building on the results from Stage II. The prior knowledge is transferred through the observation dataset.
The optimization dataset includes 150 locally collected records and 50 records each for impact, earthquake, and strong wind. The data distribution is identical or very similar to Stage II. Over time, the dataset can be gradually replaced by newly captured data for long-term optimization.
For optimization, 20 rounds of iteration were performed, achieving results equivalent to Stage II.
This demonstrates that Stage II effectively reduces the computational and energy load in Stage III.
Additionally, the maximum values in both stages are located in the same region, confirming a strong match in data distribution and validating the underlying assumption.

## Slide 30
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
03 Federated Learning for Event Classification
01
Prototype Development
03
Federated Learning for Event Classification
02
Smart Adaptive Triggering
04
Conclusions & Plans

## Slide 31
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
03 Federated Learning for Event Classification – Federated Learning
3-1 Federated Learning (FL)
…
Client 1
Client 2
Client n
Model Uploading
①
③
④
Model Aggregation
Model Distribution
Model Training
Server
①
①
②
②
②
③
③
①
②
③
④
FL Mechanism
Background and Gaps
Google 2016
Decentralized Framework
Privacy & Efficiency for IoT & Mobile Devices
Few Studied FL in IoT-based SHM, not to mention MCU devices
Features
Localized Data Usage, No Raw Data Transmission
Energy-Efficient
Privacy-Preserving
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
Challenges: (1) Onboard Training; (2) Multi-Node Coordination
Notes: Federated Learning, is introduced by Google in 2016, is a typical decentralized framework aiming at privacy and efficiency issues for IoT and mobile devices.
In the domain of Structural Health Monitoring (SHM), very few studies have tried Federated Learning, not to mention on resource constrained devices.
Federated Learning features::
local data usage and no raw data transmission.
It is energy-efficient and privacy-preserving.
On the right-hand side is how FL works:
The server distributes the model to the clients.
The clients train the model locally on their own data.
The clients upload their trained models back to the server.
The server aggregates the models to update the global model.
This process can be repeated for a few rounds.
As can be seen, there are two major challenges in this process: (1) onboard training and (2) coordination

## Slide 32
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
03 Federated Learning for Event Classification – Event Classification & 1D CNN Network
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
3-2 Event Classification & 1D CNN Network
Event Classification
Structures
Responses
Events
Newmark-Beta
Equation of Motion
AV
IP
EQ
SW
1D Convolutional Neural Network
Model Selection
Long-Short-Term Memory Network (1D / Time-Consuming)
Convolutional Neural Network (CV-2D / TS-1D )
Feature Engineering
Lightweight
Knowledge Embedding
Signal (6000 points)
Time Domain
Frequency Domain
Down Sampling (128 points)
Lightweight 1D CNN Classifier
Conv + BN + ReLu
1x128x4
Avg Pooling
1x1x4
FC
1x1x4
Label
1x1x1
Signal + Filters
1x128x1 | 1x3x4
4x3+4
4x4+4
4x2
4x2
44
8
Notes: Federated Learning is a training paradigm, not an algorithm.
For event classification, still, we focus on four types of events and their structural responses.
For NN model, after selection, 1D CNN model is selected to be used as a baseline.
One critical step for light-weight is feature engineering, which can make the model lightweight by embedding domain knowledge. Using time- and frequency-domain features and down-sampling, we reduce a signal from 6000 samples to as few as 128 samples.
After that, a lightweight 1D CNN with only 44 trainable parameters is used for classification, ensuring both efficiency and accuracy.

## Slide 33
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
03 Federated Learning for Event Classification – Event Classification & 1D CNN Network
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
3-2 Event Classification & 1D CNN Network
Confusion Matrix
206
213
194
179
Performance on Test Set (800 Samples )
Training Set Size (2400 Samples) | Validation (800 Samples)
Training Curve
Test Acc > 99%
Notes: Though lightweight, the CNN model has a good performance for classification.
Used as a baseline model for FL.

## Slide 34
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
03 Federated Learning for Event Classification – Federated Learning for Event Classification
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
3-3 Federated Learning for Event Classification
Credits
Thang Khan Khual
Chen Yong Han, John
Devices for Implementation
Setup
RPI 1
Laptop
Parameter Averaging
Local
Training
RPI 2
Local
Training
Training: 30720
Testing: 7680
Total: 38400
Training: 3072
Testing: 768
Total: 3840
Notes: The FL part was finished in collaboration with two FYP students, Khual and John, and I want to thank them for their contributions.
In this study, a laptop was used to simulate the server, while two Raspberry Pi devices acted as the clients.
The specifications of these devices are shown in the table.
The simulation setup is displayed on the right-hand side. Note that size of dataset is different to simulate a common case in reality.

## Slide 35
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
03 Federated Learning for Event Classification – FL Simulation
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
3-4 FL Simulation
Simulation Framework
Python-based Web Framework
Communication
Hypertext Transfer Protocol (HTTP)
FL Flowchart
Notes: The programming part is based on Flask, a python-based web framework, and the communication is completed by HTTP protocol.
On the right-hand side is the flow chart for FL simulation, showing many technical considerations.

## Slide 36
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
03 Federated Learning for Event Classification – Results and Discussion
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
3-5 Results & Discussion
Model Training – Client 1 – With FL (5 rounds)
Test Acc 99.63%
Model Training – Client 1 – Without FL
Test Acc 99.64%
Model Training – Client 2 – With FL (5 rounds)
Test Acc 99.19%
Model Training – Client 2 – Without FL
Test Acc 99.19%
Baseline Model vs Federated Learning Model Performance - Comparable
Notes: And here are the results.
These pictures are about the training process when training the baseline model without FL.
These pictures are about the training process when training the model with FL.
As can be seen, the model performance are quite similar, showing that FL will not introduce difference into model performance.

## Slide 37
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
03 Federated Learning for Event Classification – Results and Discussion
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
3-5 Results & Discussion
Transmission Over Head – Significantly Reduced !
Model Training Transmission – Without FL
Number of Records x Points Per Record x Bytes Per Point
(38400 + 3840) x 6000 x 4 = 966.80 MB ~ 1 GB
Model Training Transmission – FL (5 rounds)
Trainable Parameter 44 (176B) | Optimizer Parameter 90 (360B)
Communication Overhead: 4.14 KB
  Round 1 Distribution
    536B x 2 = 1072B
  Round 1 Uploading + Round 2-5 Distribution & Uploading
    176B x 2 x 9 = 3168B
4.14KB / 1GB = 0.00042%
To Do
MPU > MCU
Onboard Training
Multi-node Coordination
Notes: Now, let’s estimate the communication payload for these two training paradigms.
Without FL, all raw data must be sent to a remote server, resulting in a payload of about 1GB—this means high power consumption and latency.
With FL, assuming 5 training rounds, the payload is only about 4 KB, which is significantly smaller. This highlights the potential of FL for IoT systems.
Looking ahead, there’s still much to be done. Currently, the mechanism runs on MPU devices, but we aim to move to MCU devices, which presents new challenges:
Onboard training: MCU devices lack proper tools for training.
Multi-node coordination: Efficient tools are needed for communication.
Once completed, we’ll conduct a more detailed evaluation, focusing on communication overhead, power consumption, and latency.

## Slide 38
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
04 Conclusions & Plans
01
Prototype Development
03
Federated Learning for Event Classification
02
Smart Adaptive Triggering
04
Conclusions & Plans

## Slide 39
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
04 Conclusions & Plans – Conclusions
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
4-1 Conclusions
Prototype Development
Algorithm Development
Sensor Node - LiftNode
Low-Price Low-Power Sensing Node
Layered & Modularized
Validated In Projects
Framework - TinySHM
Edge Intelligence Powered SHM Applications
Low-cost Low-Power Devices
Long-Term Large-Scale Autonomous
Smart Adaptive Triggering Mechanism
Feedback Control, Digital Twin, NN, Bayesian Optimization
Adaptive Fast-convergence Parameter Optimization
Federated Learning for Event Classification
Federated Learning Framework for Event Classification
Great Potential to Reduce Communication Overhead and Power Consumption
Notes: Prototyping: This research focuses on developing a framework for edge intelligence-powered SHM applications on low-cost, low-power devices, enabling long-term, large-scale autonomous sensing.
To support and validate this framework, a low-cost, low-power sensor node has been prototyped with a layered and modularized software architecture. Its effectiveness has been demonstrated in multiple projects.
Algorithm Development: This research introduces a smart adaptive triggering mechanism that integrates feedback control, digital twin models, neural networks, and Bayesian Optimization to achieve fast-convergence parameter optimization for event triggering.
Additionally, a federated learning workflow for SHM event classification is proposed, showing significant potential to reduce communication overhead and power consumption.

## Slide 40
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
04 Conclusions & Plans – Publications & Future Plans
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
SHUAIWEN CUI
4-2 Publications & Future Plans
Publications
[1] Cui, S., Hoang, T., Mechitov, K., Fu, Y., & Spencer, B. (2024). Adaptive Edge Intelligence for Rapid Structural Condition Assessment using a Wireless Smart Sensor Network. Engineering Structures. (Accepted)
[2] Cui, S., Fu, H., Shen, W., Yu, X., Zhang, Q., & Fu, Y. (2024). Computing in IoT-based Structural Health Monitoring: A Review. TBD. (Finalizing)
[3] Cui, S., Fu, H., & Fu, Y. (2024). Revolutionizing Trigger Sensing with Edge Intelligence: Staged and Adaptive Solution for Accuracy and Energy-efficiency. TBD. (Under Preparation)
Plans
Prototyping – LiftNode & TinySHM
To Be Refined and Expanded for More Functions
Federated Learning for Event Classification
MCU Deployment: Onboard Training & Coordination
More Distributed Edge Intelligence Approaches
Multi-Agent System
Notes: Till now, I have one paper got accepted, and two under preparation.
As for future studies:
First, the prototyping part will be continued.
Second, the FL learning part will move onto MCU devices, focusing on onboard training and multimode coordination.
Thirdly, I will explore more edge intelligence approaches, for example, multi-agent system.
And here is the timeline for my PhD study.

## Slide 41
THANKS FOR LISTENING!
SHUAIWEN CUI
SHUAIWEN001@e.ntu.edu.sg
School of Civil and Environmental Engineering
Nanyang Technological University
MCU NODE (ESP32)
MCU NODE (STM32)

## Slide 42
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – IoT Architecture

## Slide 43
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – IoT Architecture

## Slide 44
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Confusion Matrix

## Slide 45
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – STM32

## Slide 46
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – STM32

## Slide 47
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – STM32

## Slide 48
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – STM32

## Slide 49
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Digital Twin

## Slide 50
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Feedback Control

## Slide 51
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Deployment

## Slide 52
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Testbed

## Slide 53
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Environment

## Slide 54
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Bayesian Optimization

## Slide 55
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Bayesian Optimization
Bayesian Optimization Algorithm Framework
threshold
duration
Black Box Problem
Expensive Evaluation
Bayesian Optimization
Controller
Require：
for to T do
InitSample()
p() FitModel()
end for
function / variable domain / acquisition function / surrogate model
initialize the observation set
surrogate model regression
determine next point to investigate
get corresponding value
update the observation set
– variable domain (threshold, duration)
– the real objective function
– observation dataset, {, , …, }
– acquisition function, to determine the next point to observe, need to trade-off between exploitation and exploration
– the surrogate model, typically modelled as Gaussian Process
New Point Observation (, )

## Slide 56
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – GPR Kernel

## Slide 57
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Sampling Function

## Slide 58
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Smart Adaptive Triggering Mechanism Stage I
Data Synthesizing
Simulated
Excitation
Real
Excitation
Digital Structure
Physical Structure
Simulated
Response
Real
Response
Synthesized
Response
threshold
duration
Triggering Mechanism
Feature Engineering
AI Model Training
Feature
Label
CNN
Classifier
Noise Level
Threshold
Duration
Recall
DNN
Estimator
Time Domain
& Frequency Domain
Physical World
Legend
Virtual World
Key Results

## Slide 59
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Smart Adaptive Triggering Mechanism Stage II
ENVIRONMENT – EXCITATION & STRUCTURE & RESPONSE
SYSTEM – TRIGGERING MECHANISM
Synthesized
Excitation
Digital Twin
Structure
Structure
Response
threshold
duration
Triggering Mechanism
CONTROLLER – BAYESIAN OPTIMIZATION
SURROGATE MODEL - GPR
BAYESIAN OPTIMIZATION
duration
threshold
duration
ESTIMATOR – F-BETA CALCULATION
PRECISION
TP
TP + FP
RECALL
TP + FN
P
TP
R
threshold
duration
Reference
threshold
TP, FP, FN
Legend
Virtual World
Virtual Dataflow

## Slide 60
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Smart Adaptive Triggering Mechanism Stage III
SYSTEM – TRIGGERING MECHANISM
threshold
duration
Triggering Mechanism
ESTIMATOR – F-BETA CALCULATION
PRECISION
TP
TP + FP
RECALL
P
R
R
FEATURES
PREPROCESS
THRESHOLD
DURATION
NOISE LEVEL
CONTROLLER – BAYESIAN OPTIMIZATION
SURROGATE MODEL - GPR
BAYESIAN OPTIMIZATION
duration
threshold
duration
ENVIRONMENT – EXCITATION & STRUCTURE & RESPONSE
Real Excitation
Events
Noise
Synthesized Excitation
Events
Noise
Digital
Structure
Real
Structure
Synthesized
Response
Real
Response
Reference
threshold
threshold
duration

## Slide 61
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – NN Training (DNN – precision & recall)

## Slide 62
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Optimization Parameters

## Slide 63
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – FL Confusion Matrices

## Slide 64
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – FL Histograms

## Slide 65
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Anomaly Detection

## Slide 66
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Anomaly Detection

## Slide 67
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Anomaly Detection

## Slide 68
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Displacement Estimation

## Slide 69
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Bridges

## Slide 70
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Examples

## Slide 71
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Examples

## Slide 72
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Examples

## Slide 73
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Sudden Damage Detection

## Slide 74
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Sudden Damage Detection

## Slide 75
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Sudden Damage Detection

## Slide 76
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Sudden Damage Detection

## Slide 77
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Sudden Damage Detection

## Slide 78
SHUAIWEN CUI
NANYANG TECHNOLOGICAL UNIVERISITY | SINGAPORE
SHUAIWEN CUI
Distributed Edge Intelligence Enabling Framework for IoT-based Structural Health Monitoring
Appendix – Sudden Damage Detection